## Slide 1: Beginning Assembly
Poorly Presented by
Gleep

## Slide 2: What is Assembly?
The lowest level human readable machine language before machine code
Consists of mnemonic codes that represent direct processor instructions

## Slide 3: Why use Assembly?
To make small code
To make fast code
To use advanced features
To change the function of existing programs
Writing device drivers

## Slide 4: Computer Diagram
Processor
System Memory
Input
Devices
Output
Devices
Control bus
Address bus
Data bus

## Slide 5: Processor Diagram
Control Unit
Execution Unit
Registers
Flags

## Slide 6: Control Unit Diagram
Control Unit
Instruction Prefetch and Decoder
Out-of-Order Execution Engine
Retirement Unit
Branch Prediction
Execution Unit
System Memory

## Slide 7: Instruction Prefetch
Instruction Prefetch and Decoder
Branch Prediction
L1 Execution cache
Decoder
System Memory
L2 Execution cache
Out-of-Order Execution Engine

## Slide 8: Out-of-Order Execution Engine
Out-of-Order Execution Engine
Instruction Prefetch and Decoder
Retirement Unit
Execution Unit
Allocator
Register
Renaming
Micro-Ops
Scheduler
Register
Allocation
Table

## Slide 11: Memory (32 bit)
User memory is from 0x00000000 to 0x7FFFFFFFF
Kernel memory is from 0x80000000 to 0xFFFFFFFF and is not user writable
The stack grows downward to lower memory addresses
The heap grows upward from lower to higher addresses

## Slide 12: Data Types
.int 32 bit integer
.ascii ASCII string
.asciz null termed ASCII string
.byte byte
.double Double precision float
.float Single precision float
.long 32 bit integer (same as .int)
.octa 16 byte integer
.quad 8 byte integer
.short 16 bit integer
.single Single precision float (same as .float)

## Slide 13: Command Syntax Flavors
AT&T
When writing commands, source is first, destination is second Ex. MOVL $10, %EAX
Immediate data values and C variables preceded by $, registers by %
Commands use suffix to denote operand size (b – byte, w – word, l – long, q – quadword)
Indirect addressing uses ( )
Intel
When writing commands, destination is first, source is second Ex. MOV EAX, 10
Hex values use a H suffix. Ex. 80H
Memory operands prefixed by <size> ptr. Ex. byte ptr foo
Indirect addressing uses [ ]

## Slide 14: Comparison of syntax
Intel Code AT&T Code
mov eax,1 movl $1,%eax
mov ebx,0ffh movl $0xff,%ebx
int 80h int $0x80
mov ebx, eax movl %eax, %ebx
mov eax,[ecx] movl (%ecx),%eax
mov eax,[ebx+3] movl 3(%ebx),%eax
mov eax,[ebx+20h] movl 0x20(%ebx),%eax
add eax,[ebx+ecx*2h] addl (%ebx,%ecx,0x2),%eax
lea eax,[ebx+ecx] leal (%ebx,%ecx),%eax
sub eax,[ebx+ecx*4h-20h] subl -0x20(%ebx,%ecx,0x4),%eax

## Slide 15: General Registers (32 bit)
EAX – Accumulator for operands and results data
EBX – Base - pointer to data in data memory segment
ECX – Counter for string and loop operations
EDX – Data – I/O pointer
ESI – Source – pointer for source of string operations
EDI – Destination – pointer for destination of string operations
ESP – Stack Pointer – tracks the top of the stack
EBP – Base Pointer – tracks the base of the stack
EIP – Instruction Pointer – keeps track of next instruction location to be executed
For 64 bit systems, change the E for R, and for 16 bit systems, remove the E.

## Slide 17: Instruction Pointer
EIP points to the address of the next instruction to be executed
Cannot be directly modified (ex. Movl EvilEIP, %EIP). Must use normal program control, such as JMP to change it
In flat memory model, EIP will be linear address 0xAAAAAAAA
In segmented memory model, EIP will be logical address CS:<offset>

## Slide 18: Segment Registers
Flat memory model – all instructions, data, and stack are in the same address space. Address location accessed with linear address
Segmented memory model – instructions, data, and the stack are in separate memory segments. Memory is accessed with logical segment address and an offset
Real Address memory model – all instructions, data, and stack are accessed by linear address

## Slide 19: Segment Registers
CS – Code segment
DS – Data segment
SS – Stack segment
ES – Extra segment pointer
FS – Extra segment pointer
GS – Extra segment pointer
All segment registers 16 bits

## Slide 20: EFLAGS
Single 32 bit register for status, control and system flags
CF – Bit 0 – Carry flag – when unsigned op result is too big or small for dest, flips to 1
PF – Bit 2 – Parity flag – if op result has even # of 1’s, flips to 1
AF – Bit 4 – Adjust flag
ZF – Bit 6 – Zero flag – Flips to 1 if op result = 0
SF – Bit 7 – Sign flag – flips to 1 if result is negative
OF – Bit 11 – Overflow flag – flips to 1 when signed op result is too big or small for dest
DF – Bit 10 – Direction flag – when 1, decrements down stack

## Slide 21: Opcodes
Hex Strings that correspond to a mnemonic command
0x90 is the opcode for No Operation (NOP)
0xCC is the opcode for a breakpoint
New opcodes added for every new processor
Exploits are usually written in opcodes, can be generated by tools like Metasploit

## Slide 22: The Stack
A section of memory used to store variables before or at runtime
Last In, First Out model
Grows from higher memory addresses to lower ones
Data is Pushed onto the top of the stack and Popped off the top of the stack
The top of the stack is managed by ESP register
The bottom of the stack frame is managed by EBP register

## Slide 24: The Heap
A section of memory used to store dynamically assigned variables, data, and objects
Random access model
Can be allocated and deallocated in runtime
Grows from lower memory addresses to higher ones

## Slide 25: Compiling
Object Code
Source Code
Compiler
Object Code
Object Library
Linker
Executable

## Slide 26: Hello World
SECTION .data
Msg: db "Hello, World!", 10
MsgLen: equ $-Msg
SECTION .bss
SECTION .text
global _start
_start:
  nop
  mov eax,4
  mov ebx,1
  mov ecx, Msg
  mov edx, MsgLen
  int 80H
  mov eax,1
  mov ebx,0
  int 80H
<- Variables with assigned values go here
<- Msg: variable declared
<- MsgLen: declared = to size of Msg
<- Unassigned memory goes here
<- Main code section
<- global command
<- code start
<- No Operation
<- Begin moving values into registers for system call
<- Print to Stdout System call
<- Move values to regs for system call
<- System call for Exit

## Slide 27: Unconditional Branching
JMP <operand>
  3 types… Short, Near, Far
  Equivalent of Goto:
  Short JMP is less that 128 bytes
  Far JMP is to another code segment
  Near JMP is everything else
  Takes one memory label as a parameter
Call <operand>
  Equivalent to function call in C
  Call pushes EIP to stack
  Call returns to main with the RET command

## Slide 28: Unconditional Branching Cont’d
Interrupt
  Hardware – used for I/O functions
  Software
    Used for accessing kernel functions
    In Linux, uses Interrupt 0x80
    In Windows, uses Interrupt 0x21
    Parameters in registers determine which function is being called with what parameters
    Ex: MOVL $1, %EAX
      MOVL $0, %EBX
      INT $0x80

## Slide 29: Stack Operations
PUSHx <source>
POPx <destination>
PUSHA/POPA – pushes/pops all 16 bit regs
PUSHAD/POPAD – pushes/pops all 32 bit regs
PUSHF/POPF – pushes/pops lower 16 bits of EFLAGS
PUSHFD/POPFD – pushes/pops full 32 bits of EFLAGS
PUSHA pushes DI, SI, BP, BX, DX, CX, and AX in order. POPA takes them from stack in reverse

## Slide 30: Comparison
CMP <op1>, <op2> - sets EFLAGS by subtracting OP1 from OP2, but does not modify either operand
TEST <op1>, <op2> - sets EFLAGS by ANDing op1 and op2, but does not modify either operand
In Intel syntax, it is CMP or TEST <operand 2>, <operand 1>
If OP2 = OP1, ZF is set to 1, CF is set to 0
If OP2 < OP1, ZF is set to 0, CF is set to 1
If OP2 > OP1, ZF is set to 0, CF is set to 0

## Slide 31: Exchanging Data
XCHG <op1>, <op2> - swaps data between regs or memory, ops must be same size
BSWAP <reg> - swaps bytes within a reg, makes big-endian into little-endian and back
XADD <src>, <dst> - exchanges src and dst, adds them, then stores result in dst. Src must be reg, dst can be reg or memory
CMPXCHG <src>, <dst> - if src & dst are =, stores src in dst. If not =, dst is stored in EAX
CMPXCHG8B <dst> - works on 64 bit vals

## Slide 32: Logical Operators
AND <op1>, <op2> - logical ANDs op1 and op2
OR <op1>, <op2> - logical ORs op1 and op2
XOR <op1>, <op2> - logical XORs op1 and op2
XORing anything with itself will set it to zero. Ex. XOR %EAX, %EAX will set %EAX to 0

## Slide 33: Moving Data
MOVx <src>, <dst> - moves src to dst
LEA <src>, <dst> – Load Effective Address loads src memory address to dst
MOVL 4(%EBX), %EAX – loads 32 bits of data at memory address %EBX+4 into %EAX
LEA 4(%EBX), %EAX – loads memory address of %EBX+4 into %EAX

## Slide 34: Bit shifting
SHL <dst>, <count> - shifts bits left by count, CF flag contains last bit to be shifted out
SHR <dst>, <count> - shifts bits right by count, CF flag contains last bit to be shifted out
ROL <dst>, <count> - shifts bits left by count, shifted bits get rolled to right side of dst
ROR <dst>, <count> - shifts bits right by count, shifted bits get rolled to left side of dst

## Slide 35: Conditional Moves - Unsigned
CMOVA/CMOVNBE <src>, <dst> - moves src to dst if above/not below or equal – (CF or ZF) = 0
CMOVAE/CMOVNB – moves src to dst if above or equal/not below – CF = 0
CMOVNC – moves src to dst if CF = 0
CMOVB/CMOVNAE – moves src to dst if below/not above or equal – CF = 1
CMOVC – moves src to dst if CF = 1
CMOVBE/CMOVNA – moves src to dst if below or equal/not above – (CF or ZF) = 1
CMOVE/CMOVZ – moves src to dst if equal/zero – ZF = 1
CMOVNE/CMOVNZ – moves src to dst if not equal/not zero – ZF = 0
CMOVP/CMOVPE – moves src to dst if PF is 1/parity is even
CMOVNP/CMOVPO – moves src to dst if PF is 0/parity is odd

## Slide 36: Conditional Moves - Signed
CMOVGE/CMOVNL <src>, <dst> - moves src to dst if greater or equal/not less than – (SF xor OF) = 0
CMOVL/CMOVNGE – moves src to dst if less/not greater than or equal – (SF xor OF) = 1
CMOVLE/CMOVNG – moves src to dst if less than or equal/not greater than – ((SF xor OF) or ZF) = 1
CMOVO – moves src to dst if OF = 1
CMOVNO – moves src to dst if OF = 0
CMOVS – moves src to dst if SF = 1
CMOVNS – moves src to dst if SF = 0

## Slide 37: Conditional JMPs
JZ <label> – JMP if ZF is set
JNZ <label> – JMP if ZF is not set
JGE <label> – JMP if equal or greater
JLE <label> - JMP if less than or equal
There’s a bunch of em… use the Googles

## Slide 38: Maths
ADD <src>, <dst> - adds src to dst, stores in dst
SUB <src>, <dst> - subtracts src from dst, stores in dst
INC <dst> - increments dst by 1
DEC <dst> - decrements dst by 1
MUL <value> - multiplies %EAX by value, stores in %EDX:%EAX
DIV <value> - divides %EDX:%EAX by value, stores result in %EAX, remainder in %EDX
IMUL <value> - signed version of MUL
IDIV <value> - signed version of DIV