## Slide 1: Near Space Exploration
Arko

## Slide 2: About Me
Undergrad at Cal Poly Pomona
  Electrical Engineering – emphasis in control systems
Work for JPL/NASA
  Software engineer for electronic part reliability testing/reporting systems
Previous projects and work
  Omni-directional drive system robots
  Self-balancing robots
  Harsh environment sensors
  Plasma Lighting RF Ballasts
  Many self-funded projects
DISCLAMER
  I am NOT here to represent JPL/NASA, all opinions and information provided are my own and are public information.

## Slide 3: What is Near Space?
University of Tennessee, Knoxville
http://csep10.phys.utk.edu/astr161/lect/earth/atmosphere.gif
Near Space
100,000ft-ish
Space
330,000ft-ish

## Slide 4: Near Space

## Slide 5: What is a HAB?
Payload
(Radio inside)
Parachute
Balloon
Notes: - What is it (Balloon+light gas+Parachute+Payload with radios)
- Why? (Camera, Science, Radio Testing, ENV, Rocket Testing, Weather, etc)

## Slide 6: What is a HAB?
~100,000ft
0ft
Notes: - What is it (Balloon+light gas+Parachute+Payload with radios)
- Why? (Camera, Science, Radio Testing, ENV, Rocket Testing, Weather, etc)

## Slide 7: Flight Path
Notes: - Example path
- Example prediction and why it's important to follow ascent/descent rates
- Example landing zone / recovery

## Slide 8: View from the ground

## Slide 9: History
HABEX1 HABEX2 HABEXpico (Launching in 1 hour!!)
Notes: - I will reference them throughout the talk then go into detail at the end

## Slide 10: Goals
What do you want your HAB to do?
  Launch/Track/Recover (radio test, teh lulz)
  Take pretty pictures
  Weather data
  Send stuff up to take pictures with
  Solar eclipse
  RF hackery

## Slide 11: Friends and Money
Get people to help
  looking over your design
  helping tracking
  Contributing parts, budgeting them space/mass to fly stuff
Setup a budget
  Low Cost: $100 – 300
    Simple tracker
    Small camera
  Medium Cost: $600 – $800
    Nicer radios & camera
    Science
  I’m Rich: $800 < monay
    Nicer Radios
    Expensive Science & etc

## Slide 12: Launch locations
Launch Location:
  Away from powerlines
  Away from public interference
  Large flat area
Landing Location (what actually determines the launch location):
  Away from large bodies of water
  Away from large mountains
  Away from military and busy airspace
  Use high altitude balloon flight path predictor

## Slide 13: Don’t step on lava or military airspace

## Slide 14: Balloon
Balloon manufacturers:
  Kaymont and Hwoyee
Designed to shred (Totex)
Calculate how much to fill: habhub.org/calc
  Neck lift  math to ascent rate/burst alt
  Consider payload mass/balloon mass
Cost: $35 - $200
Notes: - Balloon manufacturers, why the balloon are special, what they are made of, math behind ascent rate
- How to pick a balloon (target payload mass)

## Slide 15: Lifting Gas
Hydrogen
  PROS:
    Cheap ($25 - $150)
    High lift
    Very available
  CONS:
    It goes boom, so you need to be careful (avoid public areas, don’t smoke near it, common sense)
    Rate of ascent isn’t exactly constant
Helium
  PROS:
    Won’t kill you
    You can launch from almost anywhere
  CONS:
    Expensive ($50 - $300)
….You’re going to need the proper regulators

## Slide 16: Parachute
Parachutes manufactures: Spherachutes
Made of rip stop fabric
Math behind descent rate
  Drop to test
Cost: $5 - $60
- Pick parachute based on payload mass, table provided by Spherachutes (or do math)

## Slide 17: Payload Concept
Three general categories
  Pico (not too regulated, 50g UK)
  Small (FAA,CAA,CASA regulated)
  MURICA (FAA,CAA,CASA regulated)
Pico
Small

## Slide 18: MURICA

## Slide 19: Payload Comparison

## Slide 20: Payload
- Payload Camera
- You’re high, take some pictures
- Payload Science
- Take measurements, do science, test equipment
- Payload Radios
- Report position since the world is a big place
- 2-way communication for cut down and other features
Yo dawg, I’m at +34.123, -114.456 at 3000m off the ground...

## Slide 21: Payload Radio
- APRS beacon (with GPS)
- 144.390Mhz (requires HAM license)
- RTTY beacon (with GPS)
- 434.075Mhz (requires HAM license in US, no license require for UK)
- 915.075Mhz (no license require for US, required for UK)
- Cellphone (with GPS)
- SPOT (with GPS)
- RDF Beacon (Radio Direction Finder)
-FM transmitter, tone
-Requires radio, directional antenna, maps, and compass

## Slide 22: APRS (Automatic Packet Reporting System)
Specs?
Frequency: 144.390Mhz (USA)
Modulation: AFSK (Audio Frequency Shift Keying)
AX.25 protocol @ 1200baud
Who‘s listening?
A bunch of digipeaters along the United States @ 144.390Mhz
You can setup your own station
  SDR
  TNC to serial
  APRSDroid
  Ham radio with an audio output
  (connects to audio input of computer), use an AFSK decoder.

## Slide 23: APRS Coverage

## Slide 24: APRS Station
This could be:
- Chase Car Station
Ground Stations

## Slide 25: APRS Beacon
GPS
Microcontroller
Radio
NEMA PACKET
$GPGGA,123519,4807.038,N,01131.000,E,1,08,0.9,545.4,M,46.9,M,,*47
Interface Devices
Configure any GPS/Radio settings
Reformat to APRS Packet
APRS PACKET
N6ARA/WIDE1-1/WIDE2-1>S4PRTQUI,?,F0:
`.+Gl#PO/"4q}HABEX|!V%@'b|!w!u!
GPS Signal from satellites
APRS packet transmission at 144.390Mhz

## Slide 26: APRS Beacon
GPS
Microcontroller
Radio

## Slide 27: APRS Beacon – HABEX2
GPS
Microcontroller
Radio

## Slide 28: RTTY Beacon
Specs?
Frequency: 434.075Mhz-ish (UK, USA if ham licensed)
Modulation: FSK
Protocol: RTTY (Radioteletype)
Who‘s listening?
A bunch of radios along the UK @ 434.075Mhz-ish
You can setup your own station
  SDR (active filter recommended)
  Ham radio with an audio output
  (connects to audio input of computer).
  - Using “DL-FLDIGI” to decode and upload information to internet

## Slide 29: RTTY Who’s listening?

## Slide 30: Cellular based tracker
Nullspace Labs – “NSL Tracker”
DSS Circuits
Android phone
Pretty much any phone that can be programmed and has GPS
NSL Tracker
DSS Circuits – Geogram One

## Slide 31: RDF Beacon Radio Direction Finder
Beacon transmits an FM Tone
Using a directional antenna and a ham radio with a speaker
  3 samples, find the point!

## Slide 32: Payload Tips/Guidelines
Watch cho mass
  budget mass for everything
    Balloon
    Parachute
    payload radios, payload camera, payload science
  measure mass as you go
Power devices separately
Redundancy, Redundancy, Redundancy
  Different radios, powered separately
Simple designs are the best
Plenty of insulation (Expanded or Extruded Polystyrene) (Closed cell)
Learn to tie good knots
DO A CIRCUIT & SYSTEMS ANALYSIS
TEST TEST TEST TEST TEST TEST TEST TEST TEST TEST TEST

## Slide 33: Should I bring a coat?
- Near space is cold: -60C to +40C
- Near space is a near vacuum: 0.01atm (1010Pa) - 1atm (101325Pa)
- Mountains
- Lakes/rivers/H20
- Volcanos
- Expected Winds: 1-3g , 80+mph winds (releative to air pressure)
- Flight time: 1hr – 2hrs (floaters could last 24hrs+)
- Electronics don't like these things (I’ll cover this soon)

## Slide 34: Prototype & Test & Revise
Build and test prototype in normal (1atm @ 25C) and work out software bugs
Try to build two:
  Mod it, fix it
  Beat it up, test it, revise it
  Apply final revisions to flight hardware and do environmental testing
- Plan for failures (GPS signal loss, GPS chip comm loss, backup plans, resets, etc)
Flight Hardware
Test Hardware

## Slide 35: So you think you've got a HAB?
- Does it pass basic tests?
- power up, find gps, transmit position (tested on battery)
- block gps, does it go into beacon mode?
- checksums
- radio range, climb a mountain and transmit, test your ground stations
- chase the payload
- Power calculations
- measure actual lifetime
- aim for double what you expect your flight time to be
- Test your ground equipment
- software decoding ok?
- find problems and fix them now and not on launch day
- shocking how simple it is, yet it can be overlooked
- Rope useage (have a layout on how to avoid things tangling)

## Slide 36: Near Space Environment
1) Wind
- undo connections
- break things
- rip the payload apart
2) Temperature
- cold temperatures can kill hardware
3) Vacuum
- lack of air could cause parts that rely on
convection to cool to overheat
4) EMC
- your radios could crosstalk, step on each other
- signals could couple and damage
Notes: - Wind (Why? Winds can knock the payload around an undo connections, break things, rip the payload apart)
- Temperature (Why? Cold temperatures can kill hardware)
- Vacuum (Why? Lack of air could cause parts that rely on convection to cool to overheat, go over convection,conduction,radiation)
- EMC (Why? Your radios could crosstalk, step on each other, couple and damage)
- Parachute descent rate (Why? You want to get an accurate descent rate to better predictions)

## Slide 37: How to fix ENV problems
Winds:
  tie downs, hot glue, connectors, tape
Shaking:
  throw it down stairs, if it’s fine, it’s good to fly
Vacuum/Cold
  apply either Silicone, Epoxy, or Urethane conformal coating
  ghetto solution: hot glue
    thermally "lump" it together and prevent shorting and damage
EMC
  Better design RF or keep em separated (rope apart / sheilding)
  Test all the radios and equiptment together

## Slide 38: Flight Prediction
- Habhub CUSF Flight Prediction software
- http://habhub.org/predict/
Gives you estimate landing location based on
  launch location
  ascent/descent rate
  burst altitude
  using NOAA wind data
- Prediction/Simulation is only as good as the numbers you give it
- Work to get exact:
- Balloon necklift (ascent rate)
- Parachute drag (descent rate)
- Payload mass (ascent/descent rate)
- Accurate launch time
- Run predictor from multiple launch locations and have a backup or two

## Slide 39: Habhub CUSF Flight Predictor

## Slide 40: Launch/Recovery Day
Practice runs, wash out any problems
Have a checklist and packing list
Communications
  Radio net, cellphones, yelling across the desert
Give people a report with contact info/plan/etc
Note every measurement (neck lift, time of release, etc etc)
If it lands in an easy spot, ask for permission to go on property if needed
If it lands in a bad spot, regroup, figure out approach, and come back another day if you need to.

## Slide 41: HABEX 1

## Slide 42: HABEX 1

## Slide 43: HABEX 2
MicroTrak RTG HA
NSL Tracker
RDF Beacon
Hacked Canon (CHDK)
SpaceLab_00
Temp
Acc
Gyro
Mag
Pressure
Notes: HAB1200 Balloon
48” Spherachute
Payload
  Primary Radio: MicroTrak RTG High Altitude (with mods)
  Secondary Radio: NSL Tracker (cellphone based)
  Tertiary Radio: Arclight’s RDF beacon
  Science Payload: Measure temp, acc, gyro, mag, pressure
  Canon Camera using CHDK

## Slide 44: HABEX 2
Notes: - BIG TEAM

## Slide 45: HABEX 2
Notes: - BIG TEAM

## Slide 46: HABEX 2

## Slide 47: SB Search and Rescue

## Slide 48: HABEX 2 Pictures

## Slide 49: HABEX 2 Pictures

## Slide 50: HABEX 2 Pictures

## Slide 51: HABEX 2 Pictures

## Slide 52: HABEXpico
Launching outside NOW: noon to 1pm
No picture this time.. just testing a radio and doing a launch for $150

## Slide 53: UKHAS Conference 2013
Come to London!
September 7th, 2013
1 Day conference
More indepth talk about environmental testing
HAB’s & beer

## Slide 54: ZEH EHND
Special thanks to:
Nullspace Labs
HABEX2 Launch and Recovery team!
Arclight
UKHAS
More info:
  http://wiki.032.la/nsl/HABEX2
  http://ukhas.org.uk/